Secure ESP8266 MQTT poc (2019-01-29)

Overview
There are many in depth and well documented ESP8266 MQTT tutorials out there. This in not one of them. This is a brief proof of concept where “security first” is the focus, rather than an afterthought. The goal of this project is to have a documented and working secure MQTT Broker and Client, which can be used as a reference for later projects.
If you’re a first timer this project probably isn’t for you.

Source code is available at https://github.com/tsi-software/Secure_ESP8266_MQTT_poc

As an aside, this project started out as an irrigation timer so in the code you will see references to zones being turned on and off.

High Level Design

1) Secure MQTT Broker
The “Mosquitto” MQTT Broker is installed on the OpenWRT Wifi router. Running the MQTT Broker on the Wifi router is an experiment, which has so far worked just fine. However, the MQTT Broker could be run on any other computer on the same local area network (LAN). You could even run it on a Raspberry PI if performance isn’t a strict requirement.

2) Secure MQTT Client
Again, there are many tutorials on how to program the ESP8266, everyone’s favourite IoT chip, as an MQTT Client. But I did not come across any describing how to program the ESP8266 as a secure MQTT Client. As a long time software engineer I know how important security is these days.

3) AVR SPI Slave
The original plan was to connect peripherals directly to the ESP8266 data pins but I ran out of pins very quickly. Since I had an unused ATmega168 lying around I though “what the heck” and connected the two chips via SPI with the ESP8266 as the master and the ATmega as the slave. In additions to giving me a lot more data pins this scheme also gave me 5v tolerance. I’m also happy I went this route because it has led to a number of additional useful ideas, which I will come to later.

Advantages
- Secure.

Disadvantages
- Higher processing and memory requirements that leave little remaining in the ESP8266.

Future Plans
- ESP32 and ESP8266 transparent MQTT Client bridge. Via SPI and external microcontroller (e.g. ATmega188) can subscribe and publish to MQTT with all security concerns transparently taken care of by the ESP controller.

MQTT Broker secure setup
Here are the basics of how to install, configure, and secure the “Mosquitto” MQTT Broker on an already properly configured and running installation of OpenWRT <https://openwrt.org/>. However, the MQTT Broker can run on any computer on a local area network (LAN). You could even run it on a Raspberry PI if performance isn’t a strict requirement. So the following instruction should be adaptable to most modern operating systems.

1. With ssh (or similar) log into you OpenWRT router.
2. Install Mosquitto:
   ```
   opkg install mosquitto-ssl mosquitto-client-ssl libmosquitto-ssl
   ```
3. Create 'mosquitto' user if it does not already exist.
   ```
   useradd -M mosquitto
   usermod -L mosquitto
   ```
4. Create a directory to securely hold you certificates:
   *(Keys and Certificates can be generate on any computer as long as the required files are securely copied to the server and all keys are securely stored.)*
   ```
   mkdir /root/mosquitto
   chmod go-rwx /root/mosquitto
   chown mosquitto:mosquitto /root/mosquitto
   cd /root/mosquitto
   ```
5. Make sure you know your exact host name (run something like: uci show system)
6. Create CA (Certificate Authority) key and certificate for self-signing:
   *(Determine and securely store a PEM Pass Phrase, which is used to protect your CA Key)*
   ```
   x
   ```
7. Create Server Certificate:
   x
8. Create Client Certificate:
   x
9. x

Additional References:
<https://dzone.com/articles/tips-for-developing-successful-iot-application>
<http://www.steves-internet-guide.com/mosquitto-tls/>

Secure ESP8266 MQTT Client

AVR SPI Slave